## Slide 1: Reuse-Aware RRIP with Bypassing Techniques for Last-Level Cache Replacement Policies
Zachary Murtishi, ELE 548

## Slide 2: Project Objective
The objective of this project was to develop a last-level cache replacement policy with adaptive features capable of outperforming LRU and the adaptive policies discussed in two papers discussing adaptive insertion policies
  A. Jaleel, K. B. Theobald, S. C. Steely Jr. and J. Emer, "High performance cache replacement using re-reference interval prediction (RRIP)", Proc. 37th Annu. Int. Symp. Comput. Archit., pp. 60-71, 2010.
  M.K. Qureshi, A. Jaleel, Y.N. Patt, S.C. Steely Jr., J. Emer, Adaptive insertion policies for high-performance caching, in ISCA (2007a)
The ChampSim simulator with modifications made for the Cache Replacement Championship 2 was used to perform simulations for an L2 cache replacement policy using single and multi-core configurations
Test configuration
  SPEC2006 CPU benchmarks for single and multi core, Cloudsuite benchmarks for multi-core
  2MB 16-way set-associative cache for single core
  8MB 16-way set-associative cache for quad core

## Slide 3: Last-Level Cache Replacement Policies
The last-level cache is the last chance for the CPU to fetch cached data before performing a main memory access
  Main memory accesses introduce latency and take significantly more time to execute than a cache access
Last-level cache replacement policies are important for systems utilizing multiple CPU cores
  In such a system, the cache is shared and a good policy is even more important for performance gains

## Slide 4: Least Recently Used (LRU) Policies
LRU is a simple cache replacement policy intended to replace blocks that see the least reuse during their time in the cache
  All blocks inserted into a set are placed in the MRU position.
  On a hit, block is promoted to MRU
  Blocks in the LRU position are evicted
Works well for small caches and small working sets with cyclic access patterns, often used in L1 caches
However, LRU is susceptible to thrashing with large working sets
  Also not scan resistant: a scan will result in many useless blocks taking up space in a set!

## Slide 5: LRU Insertion Policy
LRU Insertion Policy attempts to improve LRU by introducing scan resistance
  Assumes all new blocks are “scans” and will not be used at the last-level cache and should be inserted at the MRU position
Does not perform well for workloads with cyclic access patterns as all new blocks are expected to see no reuse
  Thrash: cyclic workload pattern that requires more memory than can be held in the cache, preventing useful performance from the cache as useful blocks are evicted before they can be re-referenced
  Dynamic Insertion Policy offers a solution
    Bimodal Insertion Policy places incoming blocks at the LRU position with a probability of 1/32 to add thrash resistance
    Uses set dueling to allow a workload to ”choose” between Bimodal Insertion Policy and LIP to provide both scan and thrash resistance

## Slide 6: Performance of LRU Insertion Policy and Derivatives
Figure 1: Average performance of LRU Insertion Policy and derivatives for SPEC2006 benchmarks
Chart: Performance of LIP Derivative Cache Replacement Policies
| LIP | BIP | DIP (32 leader sets) | DIP (64 leader sets)
 | -1.9554 | -1.6229 | 0.57214 | 0.60179

## Slide 7: Re-Reference Interval Prediction
Re-Reference Interval Prediction seeks to ”fix” LRU with slight changes to the eviction and insertion policy
A RRPV (Re-Reference Prediction Value) table is kept for all blocks in the cache
  Set to zero upon a hit (re-reference)
  Incremented by one when another block is evicted
New blocks typically inserted with an RRPV of RRPVmax-1
  Offers scan resistance tolerant to cyclic workloads
When this RRPV value reaches its maximum, the block is evicted
  Typically a 2 or 3-bit value, compared to the 4-bit counter required for a 16-way set-associative LRU implementation

## Slide 8: RRIP Variants and Results
All variants use 2-bit RRPV
Static RRIP (SRRIP)
  Scan-resistant
  All blocks inserted at RRPVmax-1
  Keeps blocks in cache longer than LIP
Bimodal RRIP (BRRIP)
  Thrash-resistant
  p=1/32 of new blocks inserted at RRPVmax-2
  p=31/32 inserted at RRPVmax-1
Dynamic RRIP (DRRIP)
  Attempts to offer both scan and thrash resistance
  Set dueling between Static and Bimodal
Figure 2: Average performance of RRIP and derivatives for SPEC2006 benchmarks
Chart: Performance of RRIP Derivative Cache Replacement Policies
| SRRIP | BRRIP | DRRIP (32 leader sets) | DRRIP (64 leader sets)
 | 0.12929 | 0.00071429 | -0.015 | -0.020714

## Slide 9: RRIP vs LRU/LIP
LRU can be modified to approximate RRIP
  Key idea: changing insertion points and varying counter size
RRIP offers more consistent performance over LIP and derivatives
  See astar example on next slide
RRIP requires a lower hardware budget
  Scales better than LRU
  For a 16-way set-associative cache, LRU requires 4 bits per block
    Compare to 2 bits for RRPV

## Slide 10: astar Performance for LRU/RRIP
The astar benchmark performs very poorly for cache replacement policies unsuited for cyclic access patterns (i.e. policies that quickly shift blocks out of the cache)
It can be observed that performance for astar suffers by more than 30% when using LIP, but this is partly alleviated by DIP
RRIP does not suffer from any of these issues and performance closely mirrors LRU
Figure 3: Average performance of several benchmarks for the astar benchmark
Chart: Performance of astar for LIP and RRIP derivatives
| LIP | BIP | DIP | SRRIP | BRRIP | DRRIP (32) | DRRIP (64)
 | -31.54 | -27.62 | -4.33 | 0.03 | 0.06 | 0.05 | 0.04

## Slide 11: Reuse-Aware RRIP
While DRRIP offers a mix of thrash and scan resistance to improve performance over LRU, there is no way for the policy to know which blocks are seeing reuse
  We can optimize cache replacement by identifying which PC addresses are associated with instructions that result in reused blocks and insert new blocks accordingly
Uses 2-bit RRPV table to reduce hardware requirements
Reuse-Aware RRIP uses a PC-indexed table to determine if a block is seeing significant reuse and adjusts its insertion position accordingly
  Inspired by SHiP/SHiP++

## Slide 12: Reuse-Aware RRIP Insertion Policy
Insertion position determined by 4-bit confidence counter (CC) which is incremented and decremented upon cache accesses
  Decremented on cache fill rather than cache miss or eviction
    No need to store PC for use later
    Can be assumed that successful blocks will receive many hits to offset the initial decrement
  All writebacks are treated as the end of an access pattern and are inserted at the end of the RRPV chain
Condition | Change to Policy State
Writeback access | Insert block with RRPV = RPPVmax
Access associated with an instruction with CC <= 4 | Insert block with RRPV = RRPVmax
Access associated with an instruction with CC >= 10 | Insert block with RRPV = RRPVmax-2
All other accesses | Insert block with RRPV = RRPVmax-1
Cache fill to a block | Decrement CC
Cache block receives a hit | Increment CC
Figure 4: RA-RRIP policy description

## Slide 13: Reuse-Aware RRIP with Set Dueling
Set dueling between sets using the RA-RRIP policy and an LRU-like RRIP insertion policy was used to improve performance for workloads favoring LRU
  LRU-like RRIP: insert all blocks at RRPV =0
A 1-bit reuse counter indexed by lower 13 bits of PC is kept to indicate which blocks have been reused
  Set reuse bit on a hit for PC index
Blocks that are not reused or are writeback accesses do not alter the 10-bit PSEL counter
Condition | Change to Policy State
A miss to a set running RA-RRIP occurs | Increment the PSEL counter
A miss to a set running RA-RRIP occurs | Decrement the PSEL counter
A miss does not have the reuse bit set | Do not alter the PSEL counter
A miss is a writeback | Do not alter the PSEL counter
PSEL is greater than 512 | Follower sets use RA-RRIP
PSEL is less than or equal to 512 | Follower sets use LRU-like RRIP
Figure 5: DRA-RRIP policy description

## Slide 14: Set Dueling: How many sample sets?
Empirical data was used to determine the number of sample sets to be used for DRA-RRIP
128 was decided to be the ideal number of sets, as performance was more consistent among benchmarks, despite nominally better mean performance
Chart: Performance of DRA-RRIP with Varying Sample Set Sizes
| 16 sets | 32 sets | 64 sets | 128 sets | 256 sets | 512 sets
 | 1.0078 | 1.0117 | 1.0153 | 1.0151 | 1.0086 | 1.0021
Figure 6: Average performance of DRA-RRIP with varying sample set counts

## Slide 15: DRA-RRIP Performance
Chart: Comparison of Performance of Base RA-RRIP Policy and Dynamic RA-RRIP
| 456.hmmer | 434.zeusmp | 459.GemsFDTD | 464.h264ref | 435.gromacs
RA-RRIP | 0.9676 | 0.9147 | 0.9743 | 0.973 | 0.9663
DRA-RRIP | 1.0003 | 0.9973 | 1.0003 | 1.004 | 0.9918
Chart: Comparison of Cache Replacement Policies
| DIP | DRRIP | RA-RRIP | DRA-RRIP
 | 0.39429 | -0.0039286 | 0.50179 | 1.5332
Figure 7: Performance improvements from using DRA-RRIP for several benchmarks that perform poorly under RA-RRIP
Figure 8: Performance of DRA-RRIP compared to RA-RRIP, DRRIP, and DIP

## Slide 16: Bypassing: Basic, Ideal, and Intelligent
Bypassing was determined to be a pathway to performance increases if performed conservatively
  Bypasses may result in unnecessary main memory accesses, which may inhibit performance in cases where a block entry with reuse is not placed in the cache
However, not placing a block with little potential for reuse allows blocks with reuse to persist in the cache and therefore performance may benefit
Three policy adjustments tested:
  Basic: using confidence counter to determine if a block should be bypassed
  Ideal: an ideal case using runtime performance metrics
  Intelligent: using a runtime hit counter to determine suitability for bypassing
  Blocks in sample sets not bypassed to allow learning

## Slide 17: Basic Bypassing
Basic bypassing allows for bypassing by using only the confidence counter
  Bypass 70% of the time for CC = 1, bypass 100% of the time for CC = 0
Results in performance increases for benchmarks with many blocks seeing no reuse
  On average, performs slightly better
    About 0.3% better for DRA-RRIP, 0.9% better for RA-RRIP
Does not adapt to changes in a workload’s memory access patterns and will permanently bypass all blocks that reach CC = 0
  Results in poor performance for benchmarks with cyclic access patterns
Chart: Comparing Non-Bypassing RA-RRIP to Bypassing RRIP
Figure 9: Performance of RA-RRIP and DRA-RRIP with simple bypassing compared to their base policy implementations
Chart: Performance increases gained from bypassing over base policy
| Base policy | Simple bypassing
RA-RRIP | 0.50857 | 1.3714
DRA-RRIP | 1.5332 | 1.825

## Slide 18: Ideal Bypassing
Implements a state machine to use performance feedback from the CPU to inform bypassing decisions
  Requires cache logic capable of reading the CPU’s state to implement this policy, so difficult to implement in reality
  Requires hardware capable of fractional division
Alternate between short runs of bypassing and no bypassing, then run a bypassing-enabled or no bypassing policy for an extended period of time before re-assessing effectiveness of policy
Figure 10: State machine diagram for the ideal bypassing policy

## Slide 19: RA-RRIP vs DRA-RRIP with Ideal Bypassing
DRA-RRIP handily outperforms RA-RRIP when the ideal bypassing algorithm is used
  30,000 accesses led to ~2.18% improvement over LRU
Chart: Ideal bypassing: RA-RRIP vs DRA-RRIP
| 30,000 accesses | 50,000 accesses | 70,000 accesses
RA-RRIP | 1.2811 | 1.1536 | 1.2082
DRA-RRIP | 2.1789 | 2.1196 | 2.1532
Figure 11: Ideal bypassing algorithm performance compared for RA-RRIP and DRA-RRIP

## Slide 20: Results of Ideal Bypassing Algorithm
Tested three access periods for the extended bypassing period
  30,000, 50,000, and 70,000
All three cases outperform both base DRA-RRIP and DRA-RRIP with simple bypassing
  30,000 accesses resulted in a performance gain of nearly ~2.18% over LRU on average
Chart: Cache replacement policies
| DRA-RRIP | DRA-RRIP (Simple Bypassing) | Ideal (30,000 accesses) | Ideal (50,000 accesses) | Ideal (70,000 accesses)
 | 1.5332 | 1.825 | 2.1789 | 2.1196 | 2.1532
Figure 12: Ideal bypassing algorithm with several period lengths compared to other policies

## Slide 21: Intelligent Bypassing
”Intelligent” bypassing uses data collected solely from cache access patterns and state information to determine if bypassing is effective
  Thresholds derived from analysis of zeusmp and libquantum access patterns
  Bypassing is effective for blocks that do not see high degrees of reuse; hurts performance for blocks with high reuse
  Uses hit ratio of low-confidence accesses (hit/miss of accesses with CC = 0) to determine if these blocks see a high degree of future reuse
If these low-confidence accesses do not see much reuse, enable bypassing for an extended period
  If not, check again after another short period
Condition | Action
Hit ratio > THRESHOLD after 10,000 low-confidence accesses | Do not bypass, reassess in 10,000 low-confidence accesses
Hit ratio < THRESHOLD after 10,000 low-confidence accesses | Bypass for 100,000 low-confidence accesses
Figure 12: Simple description of the intelligent bypassing algorithm

## Slide 22: RA-RRIP vs DRA-RRIP with Intelligent Bypassing
It can be observed that DRA-RRIP outperforms RA-RRIP when intelligent bypassing is used
  Significant advantage: ~1% speedup over RA-RRIP for each case
Chart: Performance of RA-RRIP and DRA-RRIP with Intelligent Bypassing
| 5.0000000000000001E-3 | 0.01 | 0.02
RA-RRIP | 0.67679 | 0.74429 | 1.0775
DRA-RRIP | 1.6971 | 1.8393 | 1.9786
Figure 13: Intelligent bypassing algorithm performance compared for RA-RRIP and DRA-RRIP

## Slide 23: Results of Intelligent Bypassing
Three thresholds tested for hit ratio
  0.5%, 1%, 2%
2% performs best (about 2.0% better than LRU), approaches performance of the ideal policy
  Notable: zeusmp benchmark performs close to LRU, usually performs ~9% worse with bypassing
Chart: Comparing cache replacement policies with bypassing
| DRA-RRIP | DRA-RRIP (Simple Bypassing) | Ideal (30,000 accesses) | T=0.5% | T=1% | T=2% | T=3%
 | 1.5332 | 1.825 | 2.1789 | 1.6971 | 1.8393 | 1.9786 | 1.899
Figure 14: Average performance of the intelligent bypassing algorithm compared to several other policies using bypassing

## Slide 24: Single Core DRA-RRIP compared to Hawkeye and SHiP++
Chart: DRA-RRIP policies compared to SHiP++ and Hawkeye
| DRA-RRIP | DRA-RRIP (Intelligent bypassing) | DRA-RRIP (Ideal bypassing) | SHiP++ | Hawkeye
 | 1.5332 | 1.9786 | 2.1789 | 2.7621 | 2.5636
Policy | Performance over LRU
DRA-RRIP with Intelligent Bypassing | 1.98%
SHiP++ | 2.76%
Hawkeye | 2.56%
Figure 15: RA-RRIP policies compared to Hawkeye and SHiP++

## Slide 25: Multicore Performance of RA-RRIP and Derivatives
Multicore performance was evaluated for the best-performing variant of each configuration
  4 cores sharing an 8MB last-level cache
Policies tested using SPEC CPU2006 and Cloudsuite benchmarks
RA-RRIP and TA-DRA-RRIP tested with global bypassing (simple case), thread-aware bypassing, and no bypassing
  Global bypassing
  Thread-Aware DRA-RRIP: each policy has a unique PSEL counter to determine policy
  Thread-Aware Bypassing: bypassing is performed on a per-thread basis

## Slide 26: Multicore Performance (Cloudsuite)
Policy | Average speedup over LRU (%)
TA-DRRIP | 1.03
TA-DRA-RRIP (Intel bypass) | 3.74
Hawkeye | 3.47
SHiP++ | 4.52
TA-DRA-RRIP outperforms Hawkeye!!!!
Figure 16: Multicore performance of DRA-RRIP and derivatives compared to Hawkeye and SHiP++ for Cloudsuite benchmarks
Chart: Cloudsuite performance for Multicore Cache Replacement Policies
| Cassandra | Classification | Cloud9 | Nutch | Streaming | AMEAN
TA-DRRIP | 1.2706 | 0.42427 | 0.28388 | 0.54196 | 2.6128 | 1.0267
DRA-RRIP | 2.8448 | -0.55948 | 0.12769 | 0.41335 | 11.3193 | 2.8291
DRA-RRIP (Simple bypassing) | 4.4193 | -0.63409 | 0.21632 | 0.46609 | 6.0142 | 2.0964
DRA-RRIP (Ideal bypassing) | 3.6558 | 0.23556 | 0.15787 | 0.57082 | 12.4731 | 3.4186
DRA-RRIP (Intelligent bypassing) | 4.6711 | 0.19724 | 0.12385 | 0.38354 | 13.3123 | 3.7376
Hawkeye | 5.0207 | 0.12229 | 0.083607 | 0.28073 | 11.8443 | 3.4703
SHiP++ | 6.389 | 0.7639 | 0.34808 | 0.84696 | 14.2699 | 4.5236

## Slide 27: Multicore Performance (SPEC CPU2006)
Policy | Speedup over LRU (%)
TA-DRRIP | 1.32
TA-DRA-RRIP | 3.45
Hawkeye | 8.07
SHiP++ | 7.17
Figure 17: Multicore performance of DRA-RRIP and derivatives compared to Hawkeye and SHiP++ for SPEC CPU2006 benchmarks
Chart: Comparison of Average Multicore Performance for TA-DRA-RRIP and Derivatives
| TA-DRRIP | TA-DRA-RRIP | TA-DRA-RRIP (Simple bypassing) | TA-DRA-RRIP (Ideal bypassing) | TA-DRA-RRIP (Intelligent bypassing) | Hawkeye | SHiP++
 | 1.3162 | 3.4251 | 2.1722 | 2.6122 | 2.8849 | 8.0726 | 7.1715

## Slide 28: Hardware Budget
Policy | Single core 2MB | Multicore 8MB
LRU | 16KB | 64KB
DRRIP | 8KB + 2B | 32KB + 2B
DRA-RRIP | 18KB + 2B | 73.728KB + 5B
DRA-RRIP (Intelligent Bypassing) | 18KB + 6B | 73.728KB + 21B
Hawkeye | 31.8KB | 90.2KB
SHiP++ | 16KB | 76.25KB
Figure 18: Hardware budgets required for each policy assuming use in a 16-way set-associative cache

## Slide 29: Conclusions
RA-RRIP and DRA-RRIP offer improvements over DRRIP and LRU (and LIP derivatives) in both single and muti-core configurations
Set dueling and bypassing paired with reuse awareness are vital in achieving speedup or near-LRU performance for all memory access patterns
Hawkeye and SHiP++ outperform all policies based off RA-RRIP
  DRA-RRIP must be improved for multicore performance
  Gap is small for single core (>1%)